Energy Model

### Step-by-Step Mathematical Model
#### 1. Solar Position Calculation
To start, we need the solar position at each time step (hourly), including:
- Solar zenith angle (θz​): The angle between the sun and the vertical direction.
- Solar azimuth angle (A): The compass direction from which the sunlight is coming.
These depend on the location of the building, the day of the year, and the time of day.
For each hour, we can calculate these angles using standard solar position equations or data from a solar position library like pvlib (not in your time series file but necessary for positioning).
#### 2. Incidence Angle Calculation
Once we have the solar position, we need to compute the incidence angle (θincidence) between the sun’s rays and the solar panel. This angle depends on the tilt and azimuth of the panel, as well as the solar position.
Formula:
cos(θincidence​)=sin(θz​)sin(β)+cos(θz​)cos(β)cos(A−Ap​)
Where:
- θz is the solar zenith angle.
- β\ is the tilt angle of the panel.
- Ais the solar azimuth angle.
- Ap is the panel’s azimuth.

#### 3. Adjusting Solar Irradiance for Tilt
Next, we need to convert the solar irradiance in the time series (which is measured on a horizontal surface) to the tilted surface of the solar panels. This requires two steps: adjusting both direct and diffuse irradiance values.
##### Direct Irradiance (SolRad_Hor) on the Tilted Surface
For each hour, we use the direct horizontal irradiance (SolRad_Hor) and adjust it based on the incidence angle.
Formula:
      Idirect_tilted​=Idirect_hor​×cos(θincidence​)

Where:

Idirect_hor​ is the direct horizontal solar irradiance (from your time series data: SolRad_Hor).

θincidence​ is the incidence angle we calculated earlier.

##### Diffuse Irradiance (SolRad_Dif) on the Tilted Surface
The diffuse solar irradiance (SolRad_Dif) is spread over the entire sky, so it must also be adjusted for the tilt angle of the panels.
Formula:

Idiffuse_tilted​ = Idiffuse_hor​ x (1+cos(β)​ )/2

Where:
Idiffuse_hor​ is the diffuse horizontal irradiance (from your time series data: SolRad_Dif).

β is the tilt angle of the panel.

##### Total Irradiance on the Tilted Surface
The total solar irradiance on the tilted panel is the sum of the direct and diffuse components:
Itilted​=Idirect_tilted​+Idiffuse_tilted​

#### 4. Adjusting for Temperature Effects
The air temperature from the time series file affects the efficiency of the solar panels, which decreases as they heat up. The cell temperature Tcell of the panels is calculated using the air temperature and the solar irradiance:

Formula:

Tcell​=Tair​ + (Itilted/800) ​​×(NOCT−20)

Where:
- Tair is the air temperature (from your time series data: Air Temp).
- ItiltedI is the total irradiance on the tilted surface.
- NOCTs the Nominal Operating Cell Temperature (typically provided in the solar panel specifications).

### Modeling Wind Speed’s Effect on Panel Temperature
If we want to include the effect of wind speed on the panel temperature, we can modify the equation for cell temperature to take wind speed into account. A common approach is to add a term that incorporates wind speed in the calculation of panel temperature.
#### Updated Cell Temperature Formula with Wind Speed:

Tcell​ = Tair + (Itilted/800) ×((NOCT−20) / (1+0.1×WS))

Where:
- WS is the wind speed (from your time series data: WS_10m).
- The term 0.1×WS0.1 \times WS0.1×WS adjusts the temperature reduction based on the wind speed.
- NOCT is the Nominal Operating Cell Temperature, typically provided in the panel specifications.

#### Explanation:
- The wind speed (WS) term is added to reduce the cell temperature. As the wind speed increases, it cools the panels more, so the cell temperature decreases more quickly.
- At higher wind speeds, the cooling effect becomes more significant, reducing the impact of temperature on the panel's performance.

#### 5. Power Output Adjustment for Temperature
Once we have the cell temperature, we adjust the panel’s maximum power output Pmax using a temperature coefficient αPm that accounts for the temperature effects on the panel's performance.
Formula:

Padjusted​=Pmax​×[1+αPm​×(Tcell​−25)]

Where:
- Pmax is the rated maximum power output of the panel under standard test conditions (STC).
- αPm​ is the temperature coefficient of power (typically given by the manufacturer).
- Tcell is the panel's operating cell temperature.

#### 6. Final Power Output Calculation
Finally, we calculate the actual power output of the panel using the efficiency of the solar panel and the tilted irradiance.
Formula:

Poutput = η × Padjusted × (Itilted/1000)

Where:
- η is the panel’s efficiency (typically given as a percentage, e.g., 14.6%).
- Padjusted​ is the maximum power output adjusted for temperature.
- Itilted​ is the total irradiance on the tilted surface.
- The factor 1/1000 is used to convert from watts per square meter (W/m²) to kilowatts per square meter (kW/m²).

### Summary of Where the Time Series Data is Used
1. Air Temp:
  1. Used to calculate the cell temperature and adjust the panel’s efficiency.
2. SolRad_Hor (Direct Horizontal Irradiance):
  1. Used to calculate the direct irradiance on the tilted surface.
3. SolRad_Dif (Diffuse Irradiance):
  1. Used to calculate the diffuse irradiance on the tilted surface.
4. WS_10m (Wind Speed):
  1. Can be used for more advanced cooling models, where wind can help reduce the temperature of the panels and improve efficiency.
5. RH (Relative Humidity):
  1. This can be used in more advanced models that account for humidity impacts on sunlight attenuation (e.g., more humid air can scatter sunlight more, reducing irradiance).

### Final Power Output Formula (Simplified):
Bringing it all together, the final power output of the panel at each hour is given by:
Poutput = η × Pmax × [1+αPm × (Tcell​−25)] × (Itilted / 1000)
Where:
- Air Temp influences the cell temperature.
- SolRad_Hor and SolRad_Dif are used to compute the total irradiance on the tilted panel.
- Wind Speed and Relative Humidity may optionally be used to refine cooling or irradiance models.

## Mathematical Models Explained
### 1. Solar Position Model
Understanding the sun's position in the sky is crucial for calculating the solar irradiance on a tilted surface.
#### Key Solar Angles
- Solar Zenith Angle (θₓ): The angle between the sun's rays and the vertical.
- Solar Azimuth Angle (γₓ): The compass direction from which the sunlight is coming.
#### Calculations
1. Julian Day (JD):
  JD=Day of the year + (Hour of the day)/24
2. Declination Angle (δ):
  1. Represents the tilt of the Earth's axis relative to its orbital plane.
    δ=23.45∘ × sin(360∘× (284+n​) / 365)
  2. n: Day of the year (1 to 365)
3. Time Correction Factor (TC):
  Accounts for the equation of time and longitude differences
  1. B=(360∘/365)×(n−81)
     EOT = 9.87×sin⁡(2B)−7.53×cos⁡(B)−1.5×sin⁡(B)
     TC=4×(Longitude−Standard Meridian)+EOT
1. Local Solar Time (LST):
  LST=Local Time+(TC/60)​
2. Hour Angle (ω):
  1. The angular displacement of the sun east or west of the local meridian.
  ω=15∘×(LST−12)
3. Solar Zenith Angle (θₓ):
  cos⁡θx=sin⁡φ×sin⁡δ+cos⁡φ×cos⁡δ×cos⁡ω
  1. φ: Latitude
4. Solar Azimuth Angle (γₓ):
  sin⁡γx = (cos⁡δ × sin⁡ω)/sin⁡θx
  1. Adjustments are needed to determine the correct quadrant.
#### Usage in Code
- The pvlib.solarposition.get_solarposition function computes the solar zenith and azimuth angles using these equations internally.
- Inputs:
  - Time Index: Timestamps localized to the specific time zone.
  - Latitude and Longitude: Coordinates of the location.

### 2. Solar Irradiance Calculation
Calculating the solar irradiance on a tilted surface involves decomposing the global horizontal irradiance into its components and adjusting for the tilt and orientation of the panel.
#### Components of Solar Irradiance
1. Global Horizontal Irradiance (GHI):
  1. Total solar radiation received on a horizontal surface.
2. Direct Normal Irradiance (DNI):
  1. Solar radiation received directly from the sun on a surface perpendicular to the sun's rays.
3. Diffuse Horizontal Irradiance (DHI):
  1. Solar radiation scattered by the atmosphere and received from all directions.
#### Diffuse Models
Hay-Davies Model: Accounts for anisotropic diffuse irradiance and circumsolar brightness.
#### Calculations
1. Estimating DNI:
  1. DISC Model: Uses GHI and solar zenith angle to estimate DNI.
  DNI=Function of (GHI,θₓ)
      2. Extraterrestrial DNI (DNIₑₓₜᵣₐ):
Solar constant adjusted for Earth-Sun distance.
DNIextra = Isc × (1 + 0.033 × cos(360∘ x n)/365))

Iₛc: Solar constant ≈ 1367 W/m²

Total Irradiance on Tilted Surface (POA Global):
- Beam Component:
- Ib = DNI × cosθi
  θᵢ: Angle of incidence between the sun's rays and the panel normal.
Cosθi = sinδ * sinφp + cosδ * cosφp * cosωp
φ_p: Panel tilt angle.

ω_p: Adjusted hour angle for panel orientation.

Diffuse Component (Hay-Davies):
Id = DHI × ((1+cosφp)/2)×Fd
F_d: Anisotropy factor.

Ground Reflected Component:
Ir = (GHI − DHI − DNI × cos⁡θx) × ρg × ((1−cos⁡φp)/2)
ρ_g: Ground albedo (reflectivity), typically around 0.2.

Total POA Irradiance:
POA Global = Ib+Id+Ir

#### Usage in Code
- The pvlib.irradiance.get_total_irradiance function performs these calculations.
- Inputs:
  - Solar angles (zenith and azimuth).
  - Irradiance components (GHI, DNI, DHI).
  - Panel tilt and azimuth angles.
  - dni_extra for models like Hay-Davies.

### 3. Cell Temperature Model
The operating temperature of the solar cells affects their efficiency.
#### Sandia Model
The Sandia model estimates the cell temperature based on:
Tcell = Tambient + (POA Global/Eo) × (a + b × Uwind)
Tcell: Cell temperature (°C).
Tambient: Ambient air temperature (°C).
Eo: Reference irradiance, typically 1000 W/m².
Uwind: Wind speed at the module (m/s).
- a,b: Empirical coefficients depending on the mounting configuration.
#### Coefficients
For an open-rack, glass-glass module:
- a: -3.47
- b: -0.0594
#### Usage in Code
- The pvlib.temperature.sapm_cell function calculates the cell temperature.
- Inputs:
  - POA Global irradiance.
  - Ambient temperature.
  - Wind speed.
  - Model parameters a, b, and ΔT.
### 4. PVWatts DC Power Model
Calculates the DC power output of the solar panel.
#### Equation:
Pdc = Pdc0 × [Gpoa/Gref] × [1 + γpdc × (Tcell−Tref)]

Pdc: DC power output (W).
Pdc0: Rated DC power at reference conditions (W).
Gpoa: Plane-of-array irradiance (W/m²).
Gref: Reference irradiance, typically 1000 W/m².
γpdc: Temperature coefficient of power (1/°C).
Tcell: Cell temperature (°C).
Tref: Reference temperature, typically 25°C.

#### Usage in Code
- The pvlib.pvsystem.pvwatts_dc function calculates DC power.
- Inputs:
  - g_poa_effective (POA irradiance).
  - temp_cell (cell temperature).
  - pdc0 (rated DC power).
  - gamma_pdc (temperature coefficient).
### 5. PVWatts Inverter (AC Power) Model
Calculates the AC power output, accounting for inverter efficiency and clipping.
#### Equation
Pac = Pdc × ηinv
Pac: AC power output (W).
Pdc: DC power input to the inverter (W).
ηinv: Inverter efficiency (unitless).

#### Inverter Efficiency
The PVWatts inverter model accounts for efficiency variations and clipping:

ηinv = ηinv_nom × (Pdc/Pdc0)
ηinv_nom: Nominal inverter efficiency at reference conditions.
- Pdc0: Inverter's rated DC input power (W).
- Clipping occurs when Pdc>Pdc0 limiting Pac to the inverter's maximum capacity.

Usage in Code
- The pvlib.inverter.pvwatts function calculates AC power.
- Inputs:
  - pdc (DC power input).
  - pdc0 (inverter's rated DC input power).
  - eta_inv_nom (nominal inverter efficiency).
  - eta_inv_ref (reference inverter efficiency).

### 6. Annual Energy Production
- The annual energy production is calculated by summing the hourly AC power outputs over the year.
- Conversion to kilowatt-hours (kWh):

  Annual Energy (kWh) = ∑^N(Pac,t/1000)
    t=1

N: Number of hours in the year (typically 8760).
Pac,t: AC power output at time t.